## Slide 1: Unit -1
Introduction
[Chapter-1 & 2 from Forouzan]
Prachi Shah
IT Dept.
BVM

## Slide 2: Content
Data Communication
Networks
Protocols and Standards
Standard Organizations
Line Configuration
Topology
Transmission Modes
Categories of Networks
OSI model & TCP/IP model
Example network: The internet, X.25, Frame Relay

## Slide 3: 1. Data Communication
Data & Communication
Why is Data Communication System Required?
Effectiveness of a Data Communication System:
  Delivery
  Accuracy
  Timeliness
  Jitter
Data Representation
Text Numbers Images | Audio Video

## Slide 4: Data Communication
Components of data communication
(5)
(1)
(2) (3)
(4)

## Slide 5: 2. Networks
Data Communi-cation Network Criteria
Performance
Reliability
Security
Transit time
Response time
Throughput
Delay
Frequency of Failure
Unauthorization
Time taken by a link to recover
Networks robustness in catastrophe
Policy implementation for Recovery measures
Damage

## Slide 6: 3. Protocols & Standards
Protocols:
It is a set of rules that govern data communications.
It defines
  what is communicated
  how it is communicated
  when it is communicated
Key elements of a protocol are:
  Syntax (presentation or structure or format of the data)
  Semantics (How a particular pattern is to be interpreted, and what action is to be taken)
  Timing (when data should be sent and how fast they can be sent)

## Slide 7: 3. Protocols & Standards (Contd.)
Standards
De facto (By fact)
De jure (By law)

## Slide 8: 4. Standard Organizations
Standards Creation Committees formed by:
  Forums (work with universities and users to test, evaluate, and standardize new technologies)
  Regulatory Agencies (to protect the public interest by regulating radio, television, and wire/cable communications)
  Internet Standards (It is a formalized regulation that must be followed)
Some Standards Creation Committees are:
  International Organization for Standardization (ISO)
  International Telecommunication Union-Telecommunication Standards Sector (ITU-T)
  American National Standards Institute (ANSI)
  Institute of Electrical and Electronics Engineers (IEEE)
  Electronic Industries Association (EIA)

## Slide 9: 5. Line Configuration
Type of Connection
Point-to-Point
Multipoint

## Slide 10
Point-to-Point Line Configuration

## Slide 11
Point-to-Point Line Configuration

## Slide 12
Point-to-Point Line Configuration

## Slide 13
Multipoint Line Configuration

## Slide 14: 6. Topology
Physical Topology
Mesh
Star
Bus
Ring

## Slide 15
Mesh Topology

## Slide 16
Star Topology

## Slide 17
Bus Topology

## Slide 18
Ring Topology

## Slide 19
Tree Topology

## Slide 20
Hybrid Topology

## Slide 21: 7. Transmission Modes
Transmission Modes / Data Flow
Simplex
Half-Duplex
Full-Duplex

## Slide 22: Example: Keyboards and traditional monitors
Simplex

## Slide 23
Half-Duplex
Example: Walkie-talkies and CB (citizens band) radios

## Slide 24
Full-Duplex
Example: Telephone network

## Slide 25: 8. Categories of Networks
LAN
(Local Area Network)
WAN
(Wide Area Network)
MAN
(Metropolitan Area Network)
Three Categories of Networks

## Slide 26
Local Area Network

## Slide 27
Local Area Network

## Slide 28
Metropolitan Area Network

## Slide 29
Wide Area Network

## Slide 30
Internetwork
(Internet)

## Slide 31
THE
OSI
MODEL
9.1

## Slide 32
ISO is the organization. OSI is the model.

## Slide 33
OSI Model

## Slide 34
OSI layers

## Slide 35
Headers are added to the data at layers 6, 5, 4, 3, and 2. Trailers are usually added only at layer 2.

## Slide 36
An exchange using the OSI model

## Slide 37
LAYERS
IN
THE
OSI
MODEL

## Slide 38
Physical Layer

## Slide 39
Data Link Layer

## Slide 40
Node-to-node delivery

## Slide 41
Network Layer

## Slide 42
End-to-end delivery

## Slide 43
Transport Layer

## Slide 44
Reliable end-to-end delivery of a message

## Slide 45
Session Layer

## Slide 46
Presentation Layer

## Slide 47
Application Layer

## Slide 48
Summary of layers

## Slide 49: OSI Model in Short

## Slide 50
Connection Oriented Services | Connection Less Services
A connection is to be established before starting the communication | Each message is routed independently from source to destination
Authentication is needed | Does not need any authentication
Makes a connection and checks whether message is received or not and sends again if an error occurs | Does not guarantees a delivery
More reliable than connectionless service | Less reliable than connection oriented service
Connection oriented service interface is stream based | Connectionless service is message based

## Slide 51
TCP/IP
PROTOCOL
SUITE
9.2

## Slide 52
TCP/IP PROTOCOL SUITE
The layers in the TCP/IP protocol suite do not exactly match those in the OSI model.
The original TCP/IP protocol suite was defined as having four layers: host-to-network, internet, transport, and application.
However, when TCP/IP is compared to OSI, we can say that the TCP/IP protocol suite is made of five layers: physical, data link, network, transport, and application.

## Slide 53
TCP/IP and OSI model

## Slide 54
ADDRESSING

## Slide 55: Addresses in TCP/IP
Addresses
Physical addresses
Logical addresses
Port addresses
Specific addresses

## Slide 56: Relationship of layers and addresses in TCP/IP

## Slide 57
Example 1 - Physical addresses

## Slide 58
Most local-area networks use a 48-bit (6-byte) physical address written as 12 hexadecimal digits; every byte (2 hexadecimal digits) is separated by a colon, as shown below:
Example 2
07:01:02:01:2C:4B
A 6-byte (12 hexadecimal digits) physical address.

## Slide 59
Example 3 IP addresses

## Slide 60
Example 4 Port addresses

## Slide 61
Example 5
A port address is a 16-bit address represented by one decimal number as shown.
753
A 16-bit port address represented as one single number.

## Slide 62
The physical addresses change from hop to hop, but the logical and port addresses usually remain the same.
Addresses | Address Length
Physical Address | 48 bits
Logical Address | 32 bits
Port Address | 16 bits

## Slide 63: Specific Addresses:
Some applications have user-friendly addresses that are designed for that specific address.
Example : the e-mail address (for example, forouzan@fhda.edu) and the Universal Resource Locator (URL) (for example, www.mhhe.com).
The first defines the recipient of an e-mail
The second is used to find a document on the World Wide Web.
These addresses get changed to the corresponding port and logical addresses by the sending computer.

## Slide 64: 9.3 OSI v/s TCP/IP

## Slide 65: 10. Example Networks
Internet
X.25
Frame Relay

## Slide 66: 10.1) Internet
International ISP:
  Connect nations
National ISP:
  Backbone networks are connected by NAP (Network Access Points)
Regional ISP:
  They are connected to one or more national ISPs
Local ISP:
  They provide direct service to end users
  Each local ISP can be connected to a regional or national ISP
  It can be a
    company providing Internet services
    corporation with a network providing services to own employees
    nonprofit organization like college or university running their own network

## Slide 67
Hierarchical organization of the Internet