## Slide 1: Unit - 3
Data Link Layer
Prachi Shah
IT Dept.
BVM

## Slide 2: Contents
1. | Data link Layer Design Issues | [From Attached PDF]
2. | Error Detection & Correction | [From Forouzan Ch-10]
3. | Types of Errors | [From Forouzan Ch-10]
4. | Error Detection techniques: CRC & Checksum | [From Forouzan Ch-10 & Attached PDF]
5. | Error Correction techniques: Hamming Code | [From Forouzan Ch-10 & Attached PDF]
6. | Elementary Data Link Protocols: Noiseless Channel – Simplex & Stop and wait, Noisy Channel – Simplex Protocol | [From Forouzan Ch-10 & Attached PDF]
7. | Sliding Window Protocols: Stop and wait ARQ, Go-Back-N ARQ, Selective Repeat ARQ | [From Forouzan Ch-10]
8. | Example DLL protocols: HDLC & PPP | [From Forouzan Ch-10 & Attached PDF]
9. | Protocols Verification models | [From Attached PDF]

## Slide 3
Chapter 10
Error Detection and Correction
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.

## Slide 4
10-1 INTRODUCTION
Let us first discuss some issues related, directly or indirectly, to error detection and correction.
Types of Errors Redundancy Detection Versus Correction Forward Error Correction Versus Retransmission Coding
Modular Arithmetic
Topics discussed in this section:

## Slide 5
In a single-bit error, only 1 bit in the data unit has changed.
Note

## Slide 6
Figure 10.1 Single-bit error

## Slide 7
A burst error means that 2 or more bits in the data unit have changed.
Note

## Slide 8
Figure 10.2 Burst error of length 8

## Slide 9
To detect or correct errors, we need to send extra (redundant) bits with data.
Note

## Slide 10
Figure 10.3 The structure of encoder and decoder

## Slide 11
In this book, we concentrate on block codes; we leave convolution codes to advanced texts.
Note

## Slide 12
In modulo-N arithmetic, we use only the integers in the range 0 to N −1, inclusive.
Note

## Slide 13
Figure 10.4 XORing of two single bits or two words

## Slide 14
10-2 BLOCK CODING
In block coding, we divide our message into blocks, each of k bits, called datawords. We add r redundant bits to each block to make the length n = k + r. The resulting n-bit blocks are called codewords.
Error Detection Error Correction Hamming Distance
Minimum Hamming Distance
Topics discussed in this section:

## Slide 15
Figure 10.5 Datawords and codewords in block coding

## Slide 16
The 4B/5B block coding discussed in Chapter 4 is a good example of this type of coding. In this coding scheme, k = 4 and n = 5. As we saw, we have 2k = 16 datawords and 2n = 32 codewords. We saw that 16 out of 32 codewords are used for message transfer and the rest are either used for other purposes or unused.
Example 10.1

## Slide 17
Figure 10.6 Process of error detection in block coding

## Slide 18
Let us assume that k = 2 and n = 3. Table 10.1 shows the list of datawords and codewords. Later, we will see how to derive a codeword from a dataword.
Assume the sender encodes the dataword 01 as 011 and
sends it to the receiver. Consider the following cases:
1. The receiver receives 011. It is a valid codeword. The receiver extracts the dataword 01 from it.
Example 10.2

## Slide 19
2. The codeword is corrupted during transmission, and 111 is received. This is not a valid codeword and is discarded.
3. The codeword is corrupted during transmission, and 000 is received. This is a valid codeword. The receiver incorrectly extracts the dataword 00. Two corrupted bits have made the error undetectable.
Example 10.2 (continued)

## Slide 20
Table 10.1 A code for error detection (Example 10.2)

## Slide 21
An error-detecting code can detect only the types of errors for which it is designed; other types of errors may remain undetected.
Note

## Slide 22
Figure 10.7 Structure of encoder and decoder in error correction

## Slide 23
Let us add more redundant bits to Example 10.2 to see if the receiver can correct an error without knowing what was actually sent. We add 3 redundant bits to the 2-bit dataword to make 5-bit codewords. Table 10.2 shows the datawords and codewords. Assume the dataword is 01. The sender creates the codeword 01011. The codeword is corrupted during transmission, and 01001 is received. First, the receiver finds that the received codeword is not in the table. This means an error has occurred. The receiver, assuming that there is only 1 bit corrupted, uses the following strategy to guess the correct dataword.
Example 10.3

## Slide 24
1. Comparing the received codeword with the first codeword in the table (01001 versus 00000), the receiver decides that the first codeword is not the one that was sent because there are two different bits.
2. By the same reasoning, the original codeword cannot be the third or fourth one in the table.
3. The original codeword must be the second one in the table because this is the only one that differs from the received codeword by 1 bit. The receiver replaces 01001 with 01011 and consults the table to find the dataword 01.
Example 10.3 (continued)

## Slide 25
Table 10.2 A code for error correction (Example 10.3)

## Slide 26
The Hamming distance between two words is the number of differences between corresponding bits.
Note

## Slide 27
Let us find the Hamming distance between two pairs of words.
1. The Hamming distance d(000, 011) is 2 because
Example 10.4
2. The Hamming distance d(10101, 11110) is 3 because

## Slide 28
The minimum Hamming distance is the smallest Hamming distance between all possible pairs in a set of words.
Note

## Slide 29
Find the minimum Hamming distance of the coding scheme in Table 10.1.
Solution
We first find all Hamming distances.
Example 10.5
The dmin in this case is 2.

## Slide 30
Table 10.1 A code for error detection (Example 10.2)

## Slide 31
Table 10.2 A code for error correction (Example 10.3)

## Slide 32
Find the minimum Hamming distance of the coding scheme in Table 10.2.
Solution
We first find all the Hamming distances.
The dmin in this case is 3.
Example 10.6

## Slide 33
To guarantee the detection of up to s errors in all cases, the minimum
Hamming distance in a block code must be dmin = s + 1.
Note

## Slide 34
The minimum Hamming distance for our first code scheme (Table 10.1) is 2. This code guarantees detection of only a single error. For example, if the third codeword (101) is sent and one error occurs, the received codeword does not match any valid codeword. If two errors occur, however, the received codeword may match a valid codeword and the errors are not detected.
Example 10.7

## Slide 35
To guarantee correction of up to t errors in all cases, the minimum Hamming distance in a block code must be dmin = 2t + 1.
Note

## Slide 36
A code scheme has a Hamming distance dmin = 4. What is the error detection and correction capability of this scheme?
Solution
This code guarantees the detection of up to three errors (s = 3), but it can correct up to one error. In other words, if this code is used for error correction, part of its capability is wasted. Error correction codes need to have an odd minimum distance (3, 5, 7, . . . ).
Example 10.9

## Slide 37
10-3 LINEAR BLOCK CODES
Almost all block codes used today belong to a subset called linear block codes. A linear block code is a code in which the exclusive OR (addition modulo-2) of two valid codewords creates another valid codeword.
Minimum Distance for Linear Block Codes Some Linear Block Codes
Topics discussed in this section:

## Slide 38
In a linear block code, the exclusive OR (XOR) of any two valid codewords creates another valid codeword.
Note

## Slide 39
A simple parity-check code is a single-bit error-detecting code in which n = k + 1 with dmin = 2.
Note

## Slide 40
Table 10.3 Simple parity-check code C(5, 4)

## Slide 41
Figure 10.10 Encoder and decoder for simple parity-check code

## Slide 42
Let us look at some transmission scenarios. Assume the sender sends the dataword 1011. The codeword created from this dataword is 10111, which is sent to the receiver. We examine five cases:
1. No error occurs; the received codeword is 10111. The syndrome is 0. The dataword 1011 is created.
2. One single-bit error changes a1 . The received codeword is 10011. The syndrome is 1. No dataword is created.
3. One single-bit error changes r0 . The received codeword is 10110. The syndrome is 1. No dataword is created.
Example 10.12

## Slide 43
4. An error changes r0 and a second error changes a3 .
The received codeword is 00110. The syndrome is 0. The dataword 0011 is created at the receiver. Note that
here the dataword is wrongly created due to the
syndrome value.
5. Three bits—a3, a2, and a1—are changed by errors. The received codeword is 01011. The syndrome is 1. The dataword is not created. This shows that the simple parity check, guaranteed to detect one single error, can also find any odd number of errors.
Example 10.12 (continued)

## Slide 44
A simple parity-check code can detect an odd number of errors.
Note

## Slide 45
All Hamming codes discussed in this book have dmin = 3.
The relationship between m and n in these codes is n = 2m − 1.
Note

## Slide 46
Table 10.4 Hamming code C(7, 4)

## Slide 47
Figure 10.12 The structure of the encoder and decoder for a Hamming code

## Slide 48
Table 10.5 Logical decision made by the correction logic analyzer

## Slide 49
Let us trace the path of three datawords from the sender to the destination:
1. The dataword 0100 becomes the codeword 0100011. The codeword 0100011 is received. The syndrome is 000, the final dataword is 0100.
2. The dataword 0111 becomes the codeword 0111001. The syndrome is 011. After flipping b2 (changing the 1 to 0), the final dataword is 0111.
3. The dataword 1101 becomes the codeword 1101000. The syndrome is 101. After flipping b0, we get 0000, the wrong dataword. This shows that our code cannot correct two errors.
Example 10.13

## Slide 50
We need a dataword of at least 7 bits. Calculate values of k and n that satisfy this requirement.
Solution
We need to make k = n − m greater than or equal to 7, or 2m − 1 − m ≥ 7.
1. If we set m = 3, the result is n = 23 − 1 and k = 7 − 3, or 4, which is not acceptable.
2. If we set m = 4, then n = 24 − 1 = 15 and k = 15 − 4 = 11, which satisfies the condition. So the code is
Example 10.14
C(15, 11)

## Slide 51
Figure 10.13 Burst error correction using Hamming code

## Slide 52
10-4 CYCLIC CODES
Cyclic codes are special linear block codes with one extra property. In a cyclic code, if a codeword is cyclically shifted (rotated), the result is another codeword.
Cyclic Redundancy Check Hardware Implementation Polynomials Cyclic Code Analysis
Advantages of Cyclic Codes Other Cyclic Codes
Topics discussed in this section:

## Slide 53
Table 10.6 A CRC code with C(7, 4)

## Slide 54
Figure 10.14 CRC encoder and decoder

## Slide 55
Figure 10.15 Division in CRC encoder

## Slide 56
Figure 10.16 Division in the CRC decoder for two cases

## Slide 57
Figure 10.21 A polynomial to represent a binary word

## Slide 58
Figure 10.22 CRC division using polynomials

## Slide 59
The divisor in a cyclic code is normally called the generator polynomial
or simply the generator.
Note

## Slide 60
In a cyclic code, those e(x) errors that are divisible by g(x) are not caught.
Note

## Slide 61
If the generator has more than one term and the coefficient of x0 is 1, all single errors can be caught.
Note

## Slide 62
Table 10.7 Standard polynomials

## Slide 63
10-5 CHECKSUM
The last error detection method we discuss here is called the checksum. The checksum is used in the Internet by several protocols although not at the data link layer. However, we briefly discuss it here to complete our discussion on error checking
Idea One’s Complement
Topics discussed in this section:

## Slide 64
Suppose our data is a list of five 4-bit numbers that we want to send to a destination. In addition to sending these numbers, we send the sum of the numbers. For example, if the set of numbers is (7, 11, 12, 0, 6), we send (7, 11, 12, 0, 6, 36), where 36 is the sum of the original numbers. The receiver adds the five numbers and compares the result with the sum. If the two are the same, the receiver assumes no error, accepts the five numbers, and discards the sum. Otherwise, there is an error somewhere and the data are not accepted.
Example 10.18

## Slide 65
We can make the job of the receiver easier if we send the negative (complement) of the sum, called the checksum. In this case, we send (7, 11, 12, 0, 6, −36). The receiver can add all the numbers received (including the checksum). If the result is 0, it assumes no error; otherwise, there is an error.
Example 10.19

## Slide 66
How can we represent the number 21 in one’s complement arithmetic using only four bits?
Solution
The number 21 in binary is 10101 (it needs five bits). We can wrap the leftmost bit and add it to the four rightmost bits. We have (0101 + 1) = 0110 or 6.
Example 10.20

## Slide 67
How can we represent the number −6 in one’s complement arithmetic using only four bits?
Solution
In one’s complement arithmetic, the negative or complement of a number is found by inverting all bits. Positive 6 is 0110; negative 6 is 1001. If we consider only unsigned numbers, this is 9. In other words, the complement of 6 is 9. Another way to find the complement of a number in one’s complement arithmetic is to subtract the number from 2n − 1 (16 − 1 in this case).
Example 10.21

## Slide 68
Let us redo Exercise 10.19 using one’s complement arithmetic. Figure 10.24 shows the process at the sender and at the receiver. The sender initializes the checksum to 0 and adds all data items and the checksum (the checksum is considered as one data item and is shown in color). The result is 36. However, 36 cannot be expressed in 4 bits. The extra two bits are wrapped and added with the sum to create the wrapped sum value 6. In the figure, we have shown the details in binary. The sum is then complemented, resulting in the checksum value 9 (15 − 6 = 9). The sender now sends six data items to the receiver including the checksum 9.
Example 10.22

## Slide 69
The receiver follows the same procedure as the sender. It adds all data items (including the checksum); the result is 45. The sum is wrapped and becomes 15. The wrapped sum is complemented and becomes 0. Since the value of the checksum is 0, this means that the data is not corrupted. The receiver drops the checksum and keeps the other data items. If the checksum is not zero, the entire packet is dropped.
Example 10.22 (continued)

## Slide 70
Figure 10.24 Example 10.22

## Slide 71
Sender site:
1. The message is divided into 16-bit words.
2. The value of the checksum word is set to 0.
3. All words including the checksum are added using one’s complement addition.
4. The sum is complemented and becomes the checksum.
5. The checksum is sent with the data.
Note

## Slide 72
Receiver site:
1. The message (including checksum) is divided into 16-bit words.
2. All words are added using one’s complement addition.
3. The sum is complemented and becomes the new checksum.
4. If the value of checksum is 0, the message is accepted; otherwise, it is rejected.
Note

## Slide 73
Chapter 11
Data Link Control
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.

## Slide 74
11-2 FLOW AND ERROR CONTROL
The most important responsibilities of the data link layer are flow control and error control. Collectively, these functions are known as data link control.
Flow Control Error Control
Topics discussed in this section:

## Slide 75
Flow control refers to a set of procedures used to restrict the amount of data
that the sender can send before
waiting for acknowledgment.
Note

## Slide 76
Error control in the data link layer is based on automatic repeat request, which is the retransmission of data.
Note

## Slide 78
11-3 PROTOCOLS
Now let us see how the data link layer can combine framing, flow control, and error control to achieve the delivery of data from one node to another. The protocols are normally implemented in software by using one of the common programming languages. To make our discussions language-free, we have written in pseudocode a version of each protocol that concentrates mostly on the procedure instead of delving into the details of language rules.

## Slide 79
Figure 11.5 Taxonomy of protocols discussed in this chapter

## Slide 80
11-4 NOISELESS CHANNELS
Let us first assume we have an ideal channel in which no frames are lost, duplicated, or corrupted. We introduce two protocols for this type of channel.
Simplest Protocol Stop-and-Wait Protocol
Topics discussed in this section:

## Slide 81
Figure 11.6 The design of the simplest protocol with no flow or error control

## Slide 82
Algorithm 11.1 Sender-site algorithm for the simplest protocol

## Slide 83
Algorithm 11.2 Receiver-site algorithm for the simplest protocol

## Slide 84
Figure 11.7 shows an example of communication using this protocol. It is very simple. The sender sends a sequence of frames without even thinking about the receiver. To send three frames, three events occur at the sender site and three events at the receiver site. Note that the data frames are shown by tilted boxes; the height of the box defines the transmission time difference between
the first bit and the last bit in the frame.
Example 11.1

## Slide 85
Figure 11.7 Flow diagram for Example 11.1

## Slide 86
Figure 11.8 Design of Stop-and-Wait Protocol

## Slide 87
Algorithm 11.3 Sender-site algorithm for Stop-and-Wait Protocol

## Slide 88
Algorithm 11.4 Receiver-site algorithm for Stop-and-Wait Protocol

## Slide 89
Figure 11.9 shows an example of communication using this protocol. It is still very simple. The sender sends one frame and waits for feedback from the receiver. When the ACK arrives, the sender sends the next frame. Note that sending two frames in the protocol involves the sender in four events and the receiver in two events.
Example 11.2

## Slide 90
Figure 11.9 Flow diagram for Example 11.2

## Slide 91
11-5 NOISY CHANNELS
Although the Stop-and-Wait Protocol gives us an idea of how to add flow control to its predecessor, noiseless channels are nonexistent. We discuss three protocols in this section that use error control.
Stop-and-Wait Automatic Repeat Request Go-Back-N Automatic Repeat Request Selective Repeat Automatic Repeat Request
Topics discussed in this section:

## Slide 92
Error correction in Stop-and-Wait ARQ is done by keeping a copy of the sent frame and retransmitting of the frame when the timer expires.
In Stop-and-Wait ARQ, we use sequence numbers to number the frames.
The sequence numbers are based on modulo-2 arithmetic (0,1,0,1,…).
In Stop-and-Wait ARQ, the acknowledgment number always announces in modulo-2 arithmetic the sequence number of the next frame expected.
Stop-and-Wait ARQ Protocol
OR One-bit Sliding Window Protocol

## Slide 93
Figure 11.10 Design of the Stop-and-Wait ARQ Protocol

## Slide 94
Algorithm 11.5 Sender-site algorithm for Stop-and-Wait ARQ
(continued)

## Slide 95
Algorithm 11.5 Sender-site algorithm for Stop-and-Wait ARQ
(continued)

## Slide 96
Algorithm 11.6 Receiver-site algorithm for Stop-and-Wait ARQ Protocol

## Slide 97
Figure 11.11 shows an example of Stop-and-Wait ARQ. Frame 0 is sent and acknowledged. Frame 1 is lost and resent after the time-out. The resent frame 1 is acknowledged and the timer stops. Frame 0 is sent and acknowledged, but the acknowledgment is lost. The sender has no idea if the frame or the acknowledgment is lost, so after the time-out, it resends frame 0, which is acknowledged.
Example 11.3

## Slide 98
Figure 11.11 Flow diagram for Example 11.3

## Slide 99
Assume that, in a Stop-and-Wait ARQ system, the bandwidth of the line is 1 Mbps, and 1 bit takes 20 ms to make a round trip. What is the bandwidth-delay product? If the system data frames are 1000 bits in length, what is the utilization percentage of the link?
Solution
The bandwidth-delay product is
Example 11.4

## Slide 100
The system can send 20,000 bits during the time it takes for the data to go from the sender to the receiver and then back again. However, the system sends only 1000 bits. We can say that the link utilization is only 1000/20,000, or 5 percent. For this reason, for a link with a high bandwidth or long delay, the use of Stop-and-Wait ARQ wastes the capacity of the link.
Example 11.4 (continued)

## Slide 101
What is the utilization percentage of the link in Example 11.4 if we have a protocol that can send up to 15 frames before stopping and worrying about the acknowledgments?
Solution
The bandwidth-delay product is still 20,000 bits. The system can send up to 15 frames or 15,000 bits during a round trip. This means the utilization is 15,000/20,000, or 75 percent. Of course, if there are damaged frames, the utilization percentage is much less because frames have to be resent.
Example 11.5

## Slide 102
In the Go-Back-N Protocol, the sequence numbers are modulo 2m, where m is the size of the sequence number field in bits.
The send window is an abstract concept defining an imaginary box of size 2m − 1 with three variables: Sf, Sn, and Ssize.
The send window can slide one or more slots when a valid acknowledgment arrives.
The receive window is an abstract concept defining an imaginary box of size 1 with one single variable Rn. The window slides when a correct frame has arrived; sliding occurs one slot at a time.
Go-Back-N Protocol

## Slide 103
Figure 11.12 Send window for Go-Back-N ARQ

## Slide 104
Figure 11.13 Receive window for Go-Back-N ARQ

## Slide 105
Figure 11.14 Design of Go-Back-N ARQ

## Slide 106
Figure 11.15 Window size for Go-Back-N ARQ

## Slide 107
In Go-Back-N ARQ, the size of the send window must be less than 2m;
the size of the receiver window is always 1.
Note

## Slide 108
Algorithm 11.7 Go-Back-N sender algorithm
(continued)

## Slide 109
Algorithm 11.7 Go-Back-N sender algorithm
(continued)

## Slide 110
Algorithm 11.8 Go-Back-N receiver algorithm

## Slide 111
Example 11.6
Figure 11.16 shows an example of Go-Back-N. This is an example of a case where the forward channel is reliable, but the reverse is not. No data frames are lost, but some ACKs are delayed and one is lost. The example also shows how cumulative acknowledgments can help if acknowledgments are delayed or lost. After initialization, there are seven sender events. Request events are triggered by data from the network layer; arrival events are triggered by acknowledgments from the physical layer. There is no time-out event here because all outstanding frames are acknowledged before the timer expires. Note that although ACK 2 is lost, ACK 3 serves as both ACK 2 and ACK 3.

## Slide 112
Figure 11.16 Flow diagram for Example 11.6

## Slide 113
Figure 11.17 shows what happens when a frame is lost. Frames 0, 1, 2, and 3 are sent. However, frame 1 is lost. The receiver receives frames 2 and 3, but they are discarded because they are received out of order. The sender receives no acknowledgment about frames 1, 2, or 3. Its timer finally expires. The sender sends all outstanding frames (1, 2, and 3) because it does not know what is wrong. Note that the resending of frames 1, 2, and 3 is the response to one single event. When the sender is responding to this event, it cannot accept the triggering of other events. This means that when ACK 2 arrives, the sender is still busy with sending frame 3.
Example 11.7

## Slide 114
The physical layer must wait until this event is completed and the data link layer goes back to its sleeping state. We have shown a vertical line to indicate the delay. It is the same story with ACK 3; but when ACK 3 arrives, the sender is busy responding to ACK 2. It happens again when ACK 4 arrives. Note that before the second timer expires, all outstanding frames have been sent and the timer is stopped.
Example 11.7 (continued)

## Slide 115
Figure 11.17 Flow diagram for Example 11.7

## Slide 116
Stop-and-Wait ARQ is a special case of Go-Back-N ARQ in which the size of the send window is 1.
Note

## Slide 117
Figure 11.18 Send window for Selective Repeat ARQ

## Slide 118
Figure 11.19 Receive window for Selective Repeat ARQ

## Slide 119
Figure 11.20 Design of Selective Repeat ARQ

## Slide 120
Figure 11.21 Selective Repeat ARQ, window size

## Slide 121
In Selective Repeat ARQ, the size of the sender and receiver window
must be at most one-half of 2m.
Note

## Slide 122
Algorithm 11.9 Sender-site Selective Repeat algorithm
(continued)

## Slide 123
Algorithm 11.9 Sender-site Selective Repeat algorithm
(continued)
(continued)

## Slide 124
Algorithm 11.9 Sender-site Selective Repeat algorithm
(continued)

## Slide 125
Algorithm 11.10 Receiver-site Selective Repeat algorithm

## Slide 126
Algorithm 11.10 Receiver-site Selective Repeat algorithm

## Slide 127
Figure 11.22 Delivery of data in Selective Repeat ARQ

## Slide 128
This example is similar to Example 11.3 in which frame 1 is lost. We show how Selective Repeat behaves in this case. Figure 11.23 shows the situation. One main difference is the number of timers. Here, each frame sent or resent needs a timer, which means that the timers need to be numbered (0, 1, 2, and 3). The timer for frame 0 starts at the first request, but stops when the ACK for this frame arrives. The timer for frame 1 starts at the second request, restarts when a NAK arrives, and finally stops when the last ACK arrives. The other two timers start when the corresponding frames are sent and stop at the last arrival event.
Example 11.8

## Slide 129
At the receiver site we need to distinguish between the acceptance of a frame and its delivery to the network layer. At the second arrival, frame 2 arrives and is stored and marked, but it cannot be delivered because frame 1 is missing. At the next arrival, frame 3 arrives and is marked and stored, but still none of the frames can be delivered. Only at the last arrival, when finally a copy of frame 1 arrives, can frames 1, 2, and 3 be delivered to the network layer. There are two conditions for the delivery of frames to the network layer: First, a set of consecutive frames must have arrived. Second, the set starts from the beginning of the window.
Example 11.8 (continued)

## Slide 130
Another important point is that a NAK is sent after the second arrival, but not after the third, although both situations look the same. The reason is that the protocol does not want to crowd the network with unnecessary NAKs and unnecessary resent frames. The second NAK would still be NAK1 to inform the sender to resend frame 1 again; this has already been done. The first NAK sent is remembered (using the nakSent variable) and is not sent again until the frame slides. A NAK is sent once for each window position and defines the first slot in the window.
Example 11.8 (continued)

## Slide 131
The next point is about the ACKs. Notice that only two ACKs are sent here. The first one acknowledges only the first frame; the second one acknowledges three frames. In Selective Repeat, ACKs are sent when data are delivered to the network layer. If the data belonging to n frames are delivered in one shot, only one ACK is sent for all of them.
Example 11.8 (continued)

## Slide 132
Figure 11.23 Flow diagram for Example 11.8

## Slide 133
Figure 11.24 Design of piggybacking in Go-Back-N ARQ

## Slide 134
11-6 HDLC
High-level Data Link Control (HDLC) is a bit-oriented protocol for communication over point-to-point and multipoint links. It implements the ARQ mechanisms we discussed in this chapter.
Configurations and Transfer Modes Frames Control Field
Topics discussed in this section:

## Slide 135
Figure 11.25 Normal response mode

## Slide 136
Figure 11.26 Asynchronous balanced mode

## Slide 137
Figure 11.27 HDLC frames

## Slide 138
Figure 11.28 Control field format for the different frame types

## Slide 139
Table 11.1 U-frame control command and response

## Slide 140
11-7 POINT-TO-POINT PROTOCOL
Although HDLC is a general protocol that can be used for both point-to-point and multipoint configurations, one of the most common protocols for point-to-point access is the Point-to-Point Protocol (PPP). PPP is a byte-oriented protocol.
Framing
Transition Phases
Topics discussed in this section:

## Slide 141
Figure 11.32 PPP frame format

## Slide 142
PPP is a byte-oriented protocol using byte stuffing with the escape byte 01111101.
Note

## Slide 143
Figure 11.33 Transition phases

## Slide 144
Figure 11.35 LCP packet encapsulated in a frame

## Slide 145: Protocol Verification
Finite State Machined Models
Petri Net Models

## Slide 146: Finite State Machined Models
(a) State diagram for protocol 3. (b) Transmissions.

## Slide 147: Petri Net Models
A Petri net with two places and two transitions.

## Slide 148: Petri Net Models (2)
A Petri net model for – Simplex protocol for noisy Channel