## Slide 1: Unit - 5
Network Layer
Prachi Shah
IT Dept.
BVM

## Slide 2: Contents
1. | Network Layer Design Issues | [From Attached PDF]
2. | Routing Algorithms: Shortest Path Routing, Flooding, Distance Vector Routing, Link State Routing, Broadcast, Multicast routing | [From Attached PDF as well as Forouzan Ch-22]
3. | Congestion Control Algorithms | [From Attached PDF as well as Forouzan Ch-24]
4. | Quality of Service | [Forouzan Ch-24]
5. | Example protocols: OSPF, BGP | [Forouzan Ch-22]
6. | Internet multicasting IPv4 and IPv6 | [Forouzan Ch-20]
7. | IPv4 Addresses & NAT | [Forouzan Ch-19]

## Slide 3: Network Layer Design Isues
Store-and-Forward Packet Switching
Services Provided to the Transport Layer
Implementation of Connectionless Service
Implementation of Connection-Oriented Service
Comparison of Virtual-Circuit and Datagram Subnets

## Slide 4: Store-and-Forward Packet Switching
The environment of the network layer protocols.
fig 5-1

## Slide 5: Services Provided to the Transport Layer
Services should be independent of router technology
The transport layer should be shielded from (covered with) number, type and topology of routers present
The network addresses made available to transport layer should use a uniform numbering plan, even across LANs and WANs

## Slide 6: Implementation of Connectionless Service
Routing within a diagram subnet.

## Slide 7: Implementation of Connection-Oriented Service
Routing within a virtual-circuit subnet.

## Slide 8: Comparison of Virtual-Circuit and Datagram Subnets
5-4

## Slide 9: Routing Algorithms
The Optimality Principle
Shortest Path Routing
Flooding
Distance Vector Routing
Link State Routing
Broadcast Routing
Multicast Routing

## Slide 10: The Optimality Principle
(a) A subnet. (b) A sink tree for router B.

## Slide 11: Shortest Path Routing
Also known as Dijkstra algorithm
Path length is measured using:
  Number of hops
  Geographic distance
  Other metrics like mean queueing and transmission delay

## Slide 12: Shortest Path Routing

## Slide 13: Flooding
Every incoming packet is forwarded on every outgoing link except the one it arrived on
Problem: duplicates
Constraining the flood:
  Sequencing – Each packet is uniquely numbered at the source.
  Hop count – Each time a node passes on a packet, it decrements the value by one. When its value becomes ‘0’, the packet is discarded.
  Selective flooding – Exclude unreasonable links

## Slide 14: Flooding Example

## Slide 15
Static Algorithms (Non-Adaptive)
Shortest-path routing.
Flooding.
Dynamic Routing (Adaptive Routing)
Distance vector routing.
Link state routing.

## Slide 16
In distance vector routing, each node shares its routing table with its immediate neighbors periodically and when there is a change.
Distance Vector Routing

## Slide 17
Figure 22.14 Distance vector routing tables

## Slide 18
Figure 22.15 Initialization of tables in distance vector routing

## Slide 19
Figure 22.16 Updating in distance vector routing

## Slide 20: Link State Routing
Each router must do the following:
Discover its neighbors, learn their network address.
Measure the delay or cost to each of its neighbors.
Construct a packet telling all it has just learned.
Send this packet to all other routers.
Compute the shortest path to every other router.

## Slide 21: Learning about the Neighbors
Nine routers and a LAN.
A graph model of (a).

## Slide 22: Measuring Line Cost
A subnet in which the East and West parts are connected by two lines.

## Slide 23: Building Link State Packets
(a) A subnet. (b) The link state packets for this subnet.

## Slide 24: Broadcast Routing
It is the process of “Sending a packet to all destinations simultaneously”. Various methods are:
Send packet to each destination
Flooding – point-to-point routing algorithm
Multidestination routing – new packet for each output line to be used. (Each output line will contain the destination address that are to use that line)
Spanning tree
Reverse path forwarding

## Slide 25: Broadcast Routing
Reverse path forwarding
(a) A subnet. (b) a Sink tree. (c) The tree built by reverse path forwarding.

## Slide 26: Multicast Routing
(a) A network. (b) A spanning tree for the leftmost router. (c) A multicast tree for group 1. (d) A multicast tree for group 2.

## Slide 27
Congestion control refers to techniques and mechanisms that can either prevent congestion, before it happens, or remove congestion, after it has happened.
In general, we can divide congestion control mechanisms into two broad categories:
open-loop congestion control (prevention) and
closed-loop congestion control (removal).
Congestion Control

## Slide 28
Figure 24.5 Congestion control categories

## Slide 29
Figure 24.6 Backpressure method for alleviating congestion
Figure 24.7 Choke packet

## Slide 30: Hop-by-Hop Choke Packets
(a) A choke packet that affects only the source.
(b) A choke packet that affects each hop it passes through.

## Slide 31: Other techniques
(a) Load Shedding
(b) Jitter control

## Slide 32
24-5 QUALITY OF SERVICE
Quality of service (QoS) is an internetworking issue that has been discussed more than defined. We can informally define quality of service as something a flow seeks to attain.

## Slide 33
Figure 24.15 Flow characteristics

## Slide 34
24-6 TECHNIQUES TO IMPROVE QoS
In Section 24.5 we tried to define QoS in terms of its characteristics. In this section, we discuss some techniques that can be used to improve the quality of service. We briefly discuss four common methods: scheduling, traffic shaping, admission control, and resource reservation.
Scheduling Traffic Shaping Resource Reservation
Admission Control
Topics discussed in this section:

## Slide 35: 1.1 Scheduling - FIFO
Figure 24.16 FIFO queue

## Slide 36
Figure 24.17 Priority queuing
1. 2 Scheduling – Priority queuing

## Slide 37
Figure 24.18 Weighted fair queuing
1. 3 Scheduling – Weighted Fair queuing

## Slide 38
Figure 24.19 Leaky bucket
2.1 Traffic Shaping – Leaky bucket

## Slide 39
Figure 24.20 Leaky bucket implementation

## Slide 40
Figure 24.21 Token bucket
2.2 Traffic Shaping – Token bucket

## Slide 41
A leaky bucket algorithm shapes bursty traffic into fixed-rate traffic by averaging the data rate. It may drop the packets if the bucket is full.
The token bucket allows bursty traffic at a regulated maximum rate.
Note

## Slide 42
3. Resource Reservation – RSVP Protocol
Multicast Trees
Receiver-Based Reservation
RSVP Messages
  Path messages
  Resv messages
Reservation merging

## Slide 43
Figure 24.22 Path messages

## Slide 44
Figure 24.23 Resv messages

## Slide 45
Figure 24.24 Reservation merging

## Slide 46
Figure 24.25 Reservation styles

## Slide 47
4. Admission Control
The device decides whether to accept or reject a flow, based on predefined parameters
Before processing, these parameters are checked; in order to see if, its capacity and its previous commitments to other flows, can handle the new flow.
  Capacity means in terms of bandwidth, buffer size, CPU speed etc.

## Slide 48
The Example Protocol – OSPF
Open Shortest Path First
Areas – Collection of networks, host and routers all contained within an autonomous system
Area Border routers
Backbone & Backbone routers
Virtual link
Area identification
Metric
Types of links

## Slide 49
Figure 22.24 Areas in an autonomous system

## Slide 50
Figure 22.25 Types of links

## Slide 51
Figure 22.26 Point-to-point link

## Slide 52
Figure 22.27 Transient link

## Slide 53
Figure 22.28 Stub link

## Slide 54
Figure 22.29 Example of an AS and its graphical representation in OSPF

## Slide 55
The Example Protocol – BGP
Border Gateway Protocol

## Slide 56
Figure 22.32 Internal and external BGP sessions

## Slide 57
Chapter 20
Network Layer:
Internet Protocol
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.

## Slide 58
20-2 IPv4
The Internet Protocol version 4 (IPv4) is the delivery mechanism used by the TCP/IP protocols.
Datagram Fragmentation Checksum
Options
Topics discussed in this section:

## Slide 59
Figure 20.4 Position of IPv4 in TCP/IP protocol suite

## Slide 60
Figure 20.5 IPv4 datagram format

## Slide 61
Figure 20.6 Service type or differentiated services

## Slide 62
Table 20.1 Types of service

## Slide 63
Table 20.2 Default types of service

## Slide 64
Table 20.3 Values for codepoints

## Slide 65
The total length field defines the total length of the datagram including the header.
Note

## Slide 66
Figure 20.7 Encapsulation of a small datagram in an Ethernet frame

## Slide 67
Figure 20.8 Protocol field and encapsulated data

## Slide 68
Table 20.4 Protocol values

## Slide 69
An IPv4 packet has arrived with the first 8 bits as shown:
01000010
The receiver discards the packet. Why?
Solution
There is an error in this packet. The 4 leftmost bits (0100) show the version, which is correct. The next 4 bits (0010) show an invalid header length (2 × 4 = 8). The minimum number of bytes in the header must be 20. The packet has been corrupted in transmission.
Example 20.1

## Slide 70
In an IPv4 packet, the value of HLEN is 1000 in binary. How many bytes of options are being carried by this packet?
Solution
The HLEN value is 8, which means the total number of bytes in the header is 8 × 4, or 32 bytes. The first 20 bytes are the base header, the next 12 bytes are the options.
Example 20.2

## Slide 71
In an IPv4 packet, the value of HLEN is 5, and the value of the total length field is 0x0028. How many bytes of data are being carried by this packet?
Solution
The HLEN value is 5, which means the total number of bytes in the header is 5 × 4, or 20 bytes (no options). The total length is 40 bytes, which means the packet is carrying 20 bytes of data (40 − 20).
Example 20.3

## Slide 72
An IPv4 packet has arrived with the first few hexadecimal digits as shown.
0x45000028000100000102 . . .
How many hops can this packet travel before being dropped? The data belong to what upper-layer protocol?
Solution
To find the time-to-live field, we skip 8 bytes. The time-to-live field is the ninth byte, which is 01. This means the packet can travel only one hop. The protocol field is the next byte (02), which means that the upper-layer protocol is IGMP.
Example 20.4

## Slide 73
Figure 20.9 Maximum transfer unit (MTU)

## Slide 74
Table 20.5 MTUs for some networks

## Slide 75
Figure 20.10 Flags used in fragmentation

## Slide 76
Figure 20.11 Fragmentation example

## Slide 77
Figure 20.12 Detailed fragmentation example

## Slide 78
A packet has arrived with an M bit value of 0. Is this the first fragment, the last fragment, or a middle fragment? Do we know if the packet was fragmented?
Solution
If the M bit is 0, it means that there are no more fragments; the fragment is the last one. However, we cannot say if the original packet was fragmented or not. A non-fragmented packet is considered the last fragment.
Example 20.5

## Slide 79
A packet has arrived with an M bit value of 1. Is this the first fragment, the last fragment, or a middle fragment? Do we know if the packet was fragmented?
Solution
If the M bit is 1, it means that there is at least one more fragment. This fragment can be the first one or a middle one, but not the last one. We don’t know if it is the first one or a middle one; we need more information (the value of the fragmentation offset).
Example 20.6

## Slide 80
A packet has arrived with an M bit value of 1 and a fragmentation offset value of 0. Is this the first fragment, the last fragment, or a middle fragment?
Solution
Because the M bit is 1, it is either the first fragment or a middle one. Because the offset value is 0, it is the first fragment.
Example 20.7

## Slide 81
A packet has arrived in which the offset value is 100. What is the number of the first byte? Do we know the number of the last byte?
Solution
To find the number of the first byte, we multiply the offset value by 8. This means that the first byte number is 800. We cannot determine the number of the last byte unless we know the length.
Example 20.8

## Slide 82
A packet has arrived in which the offset value is 100, the value of HLEN is 5, and the value of the total length field is 100. What are the numbers of the first byte and the last byte?
Solution
The first byte number is 100 × 8 = 800. The total length is 100 bytes, and the header length is 20 bytes (5 × 4), which means that there are 80 bytes in this datagram. If the first byte number is 800, the last byte number must be 879.
Example 20.9

## Slide 83
Figure 20.13 shows an example of a checksum calculation for an IPv4 header without options. The header is divided into 16-bit sections. All the sections are added and the sum is complemented. The result is inserted in the checksum field.
Example 20.10

## Slide 84
Figure 20.13 Example of checksum calculation in IPv4

## Slide 85
Figure 20.14 Taxonomy of options in IPv4

## Slide 86
20-3 IPv6
The network layer protocol in the TCP/IP protocol suite is currently IPv4. Although IPv4 is well designed, data communication has evolved since the inception of IPv4 in the 1970s. IPv4 has some deficiencies that make it unsuitable for the fast-growing Internet.
Advantages Packet Format Extension Headers
Topics discussed in this section:

## Slide 87
Figure 20.15 IPv6 datagram header and payload

## Slide 88
Figure 20.16 Format of an IPv6 datagram

## Slide 89
Table 20.6 Next header codes for IPv6

## Slide 90
Table 20.9 Comparison between IPv4 and IPv6 packet headers

## Slide 91
20-4 TRANSITION FROM IPv4 TO IPv6
Because of the huge number of systems on the Internet, the transition from IPv4 to IPv6 cannot happen suddenly. It takes a considerable amount of time before every system in the Internet can move from IPv4 to IPv6. The transition must be smooth to prevent any problems between IPv4 and IPv6 systems.
Dual Stack Tunneling Header Translation
Topics discussed in this section:

## Slide 92
Figure 20.18 Three transition strategies

## Slide 93
Figure 20.19 Dual stack

## Slide 94
Figure 20.20 Tunneling strategy

## Slide 95
Figure 20.21 Header translation strategy

## Slide 96
Table 20.11 Header translation

## Slide 97
19-1 IPv4 ADDRESSES
An IPv4 address is a 32-bit address that uniquely and universally defines the connection of a device (for example, a computer or a router) to the Internet.

## Slide 98
Figure 19.1 Dotted-decimal notation and binary notation for an IPv4 address

## Slide 99
Change the following IPv4 addresses from binary notation to dotted-decimal notation.
Example 19.1
Solution
We replace each group of 8 bits with its equivalent decimal number (see Appendix B) and add dots for separation.

## Slide 100
Change the following IPv4 addresses from dotted-decimal notation to binary notation.
Example 19.2
Solution
We replace each decimal number with its binary equivalent (see Appendix B).

## Slide 101
Find the error, if any, in the following IPv4 addresses.
Example 19.3
Solution
a. There must be no leading zero (045).
b. There can be no more than four numbers.
c. Each number needs to be less than or equal to 255.
d. A mixture of binary notation and dotted-decimal notation is not allowed.

## Slide 102
Figure 19.2 Finding the classes in binary and dotted-decimal notation

## Slide 103
Find the class of each address.
a. 00000001 00001011 00001011 11101111
b. 11000001 10000011 00011011 11111111
c. 14.23.120.8
d. 252.5.15.111
Example 19.4
Solution
a. The first bit is 0. This is a class A address.
b. The first 2 bits are 1; the third bit is 0. This is a class C address.
c. The first byte is 14; the class is A.
d. The first byte is 252; the class is E.

## Slide 104
Table 19.1 Number of blocks and block size in classful IPv4 addressing

## Slide 105
Table 19.2 Default masks for classful addressing

## Slide 106
Figure 19.3 A block of 16 addresses granted to a small organization

## Slide 107
In IPv4 addressing, a block of addresses can be defined as
x.y.z.t /n
in which x.y.z.t defines one of the addresses and the /n defines the mask.
Note

## Slide 108
The first address in the block can be found by setting the rightmost 32 − n bits to 0s.
Note

## Slide 109
A block of addresses is granted to a small organization. We know that one of the addresses is 205.16.37.39/28. What is the first address in the block?
Solution
The binary representation of the given address is
11001101 00010000 00100101 00100111
If we set 32−28 rightmost bits to 0, we get
11001101 00010000 00100101 0010000
or 205.16.37.32.
This is actually the block shown in Figure 19.3.
Example 19.6

## Slide 110
The last address in the block can be found by setting the rightmost 32 − n bits to 1s.
Note

## Slide 111
Find the last address for the block in Example 19.6.
Solution
The binary representation of the given address is
11001101 00010000 00100101 00100111
If we set 32 − 28 rightmost bits to 1, we get
11001101 00010000 00100101 00101111
or
205.16.37.47
This is actually the block shown in Figure 19.3.
Example 19.7

## Slide 112
The number of addresses in the block can be found by using the formula 232−n.
Note

## Slide 113
Find the number of addresses in Example 19.6.
Example 19.8
Solution
The value of n is 28, which means that number of addresses is 2 32−28 or 16.

## Slide 114
Figure 19.10 A NAT implementation

## Slide 115
Figure 19.11 Addresses in a NAT

## Slide 116
Figure 19.12 NAT address translation